## Slide 1: 2013.10.19
파란색 상자가 4096개 존재
page table을 위한 영역
0xC000 8000
1st level page table entry
1st level page table
16kb = 4bytes * 4096
0xC000 0000
0xFFFF FFFF
0xEF80 0000
Kernel Code 영역
Low mem 영역 = 760MB
Module 영역
0xBF00 0000
16MB
User 영역
0x0000 0000
0xF000 0000
Buffer 8MB
VMA영역
0xFF00 0000
TTBR 0xC000 4000
Virtual Memory Map
16MB
High mem 영역
3056MB
240MB
nr_banks
: 2
membank bank[NR_BANKS]
phys_addr
start
0x2000 0000
phys_addr
size
0x2F80 0000
highmem?
0
phys_addr
start
0x4F80 0000
phys_addr
size
0x5080 0000
highmem?
1
bank[0]
bank[1]

## Slide 2: 2013.10.19 "arch/arm/mm/mmu.c"
TTBR 0xC000 4000
=init_mm.pgd
= swapper_pg_dir
파란색 상자가 4096개 존재
page table을 위한 영역
= pgd 영역
0xC000 8000
Page table address(22bit) | options
1st level page table
pgd = 16kb
= 4bytes * 4096
Page table address(22bit) | options
H/W page table 0
H/W page table 1
static pte_t * __init early_pte_alloc(pmd_t *pmd, unsigned long addr, unsigned long prot)
Linux page table 0
1024 bytes
Linux page table 1
1024 bytes
H/W page table 0
1024 bytes
H/W page table 1
1024 bytes
2nd level page table = 4kb
1024개
Section
3072개
Page Table
Section base addr | …options…
Linux page table 1
Linux page table 0

## Slide 3: 2013.10.19 "arch/arm/mm/mmu.c"
set_pte_ext(pte, pfn_pte(pfn, __pgprot(type->prot_pte)), 0);
0x???? ?000
0x???? ?400
0x???? ?800
0x???? ?C00
Linux page table 0
Linux page table 1
H/W page table 0
H/W page table 1
Small page base addr | …..
Small page base addr | …..
Page table address(22bit) | options
Page table address(22bit) | options
Page Table
1024 bytes = 1kb

## Slide 4: 2013.10.19 "arch/arm/mm/mmu.c“, “arch/arm/mm/proc-v7-2level.S”
set_pte_ext(pte, pfn_pte(pfn, __pgprot(type->prot_pte)), 0);
cpu_v7_set_pte_ext
http://www.joinc.co.kr/modules/moniwiki/wiki.php/Site/Embedded/Documents/LinuxKernelStudyForSystemenginer/arm.mmu.html 참고
Linux page table 0
Linux page table 1
H/W page table 0
H/W page table 1
Small page base addr | …..
Small page base addr | …..
r0
Small page base addr, PA[31:12]
nG
S
AP[2]
1
TEX[2:0]
001
AP[1:0]
01
C
1
B
1
1
XN
0
Outer and Inner Write-Back, Write-Allocate
Small Page
Read-only, only at PL1 or higher
*PL0, PL1, PL2.
PL0 : User (Application)
PL1 : Supervisor (Kernel)
PL2 : Hypervisor
r3
Memory
Type [2:5]
0111
SHARED USER DIRTY PRESENT (=VALID)
NONE RDONLY FILE YOUNG
Small page base addr, PA[31:12]
0
0
XN
0
0
0
1
1
1
r1
L_PTE_MT_WRITEALLOC = 0111

## Slide 5: 2013.10.19 "arch/arm/kernel/traps.c"
void __init early_trap_init(void *vectors_base)
http://venkateshabbarapu.blogspot.kr/2012/09/interrupt-handling-in-arm.html
2013.10.26 "arch/arm/kernel/entry-armv.S"
vector_\name "arch/arm/kernel/entry-armv.S"
vector_swi "arch/arm/kernel/entry-common.S"
VMA영역
0xFFFF FFFF
0xF000 0000
0xFF00 0000
16MB
0xFFFF 0000
__vectors_start
vector_\name macro에 의해
생성되는 각 모드의 코드
0xFFFF 1000
__stubs_start
vector_swi 주소
각 vector 모드로 branch
또는 swi 수행
kuser_helper
__kuser_helper_start

## Slide 6: 2013.10.19 "arch/arm/mm/mmu.c", "arch/arm/mach-exynos/common.c"
void __init iotable_init(struct map_desc *io_desc, int nr)
exynos_init_io() == mdesc->map_io();
exynos5_map_io() == cpu->map_io(); / static struct map_desc exynos5_iodesc[]
Buffer 8MB
0xF000 0000
VMA영역
0xFF00 0000
0xF600 0000
16MB
S3C_VA_IRQ
S3C_VA_SYS
S3C_VA_MEM
S3C_VA_TIMER
S3C_VA_WATCHDOG
S3C_VA_UART
create_mapping 함수에서 생성
0xF610 0000
S3C_ADDR_CPU
0xF620 0000
0xF630 0000
0xF640 0000
0xF650 0000
0xF700 0000
svm for IRQ
svm for SYS
svm for MEM
svm for TIMER
svm for WATCHDOG
svm for UART
svm for CPU
struct static_vm *svm =
early_alloc_aligned(sizeof(*svm) * nr,
__alignof__(*svm));
Kernel Code 영역
static_vmlist LIST HEAD
vm_struct | list
S5P_VA_CHIPID
0xF800 0000
static int __init exynos_fdt_map_chipid(unsigned long node, const char *uname, int depth, void *data)
svm for CHIPID

## Slide 7: 2013.10.19 "arch/arm/mm/ioremap.c", "mm/vmalloc.c"
"arch/arm/mm/ioremap.c" : void __init add_static_vm_early(struct static_vm *svm)
"mm/vmalloc.c" : void __init vm_area_add_early(struct vm_struct *vm)
vm_struct | list
next | addr | …
vm_struct | list
vm_struct | list
vm_struct | list
vm_struct | list
vm_struct | list
vm_struct | list
vm_struct | list
vm_struct | list
next | addr | …
next | addr | …
next | addr | …
next | addr | …
next | addr | …
next | addr | …
next | addr | …
next | addr | …

## Slide 8: 2013.11.16 "mm/bootmem.c“ -미완성…-
struct zone node_zones[MAX_NR_ZONES]
static void * __init alloc_bootmem_bdata
struct pglist_data pg_data_t
struct zonelist node_zonelists[MAX_ZONELISTS]
int nr_zones
struct bootmem_data *bdata
unsigned long node_start_pfn
unsigned long node_present_pages
unsigned long node_spanned_pages
int node_id
nodemask_t reclaim_nodes
wait_queue_head_t kswapd_wait
wait_queue_head_t pfmemalloc_wait
struct task_struct *kswapd
int kswapd_max_order
enum zone_type classzone_idx
int kswapd_max_order
page table 영역
0x2000 0000
0x4F80 0000
Kernel Code 영역
node_bootmem_map
unsigned long node_min_pfn
struct bootmem_data bootmem_data_t
unsigned long node_low_pfn
void *node_bootmem_map
unsigned long last_end_off
unsigned long hint_idx
struct list_head list
Low mem 영역 = 760MB
min = bdata->node_min_pfn = 0x2 0000
max = bdata->node_low_pfn = 0x4 f800
goal = 0x6 0000
limit = 0x0
start = min = 0x2000 0000
sidx = 0x2 0000 – 0x2 0000 = 0
midx = 0x4 f800 – 0x2 0000 = 0x2 f800
physical address
struct pglist_data

## Slide 9: 2013.11.23 "mm/sparse.c"
void __init memory_present(int nid, unsigned long start, unsigned long end)
struct mem_section *mem_section[NR_SECTION_ROOTS]
unsigned long section_mem_map
unsigned long *pageblock_flags
NR_SECTION_ROOTS = 1
SECTIONS_PER_ROOT = 4096 / 8 = 512 = 0x200
NR_SECTION_ROOTS = DIV_ROUND_UP(NR_MEM_SECTIONS, SECTIONS_PER_ROOT) = 올림 우리는 항상 0
mem_section
unsigned long section_mem_map
unsigned long *pageblock_flags
unsigned long section_mem_map
unsigned long *pageblock_flags
unsigned long section_mem_map
unsigned long *pageblock_flags
8 * 512 = 4096 bytes
&mem_section[SECTION_NR_TO_ROOT(nr)][nr & SECTION_ROOT_MASK];
ex) nr 이 2인 경우
&mem_section[0][2]
512개를 메모리 할당하지만 실제론 0~15, 16개만 사용
이 함수는
mem_section[0] 에 4096 bytes 만큼 메모리를 할당하고
&mem_section[0][2] ~ &mem_section[0][9] 까지
section_mem_map = 1 로 설정
[0]
[1]
[2]
[511]
.
.
.
SECTION_MARKED_PRESENT (1UL<<0)
SECTION_HAS_MEM_MAP (1UL<<1)
SECTION_NID_SHIFT 2
usemap 을 할당함
mem_section 구조체들
처음엔 nid,
다음엔 page struct 주소
(unsigned long)(mem_map - (section_nr_to_pfn(pnum)))
확인해볼것
1. page_to_pfn
2. pfn_to_page
Pfn 이 65537 이라면
65537 / 65536(1section이 가지고 있는 page 수) = 1
mem_section[0][1] 을 참고하여 section_mem_map에 있는 page struct 주소를 가져오고
이전에 빼주었었던 pfn 값을 더해주어 주소값을 보정한다.

## Slide 10: 2013.11.23 "mm/sparse.c"
void __init sparse_init(void)
unsigned long **usemap_map
[0]
[1]
[2]
4 * 16
= 64bytes
32 bytes = 256 bits = 4bits * 64
usemap은 64개의 pageblock 를 관리
1개의 pageblock이 1024개 page 관리
즉, usemap은 64 * 1024 = 65536 page를 관리
1 section은 256MB이고, 65536 page를 가짐
65536 / 1024 = 64 의 pageblock으로 구성됨
1개의 pageblock을 위한 flag는 4bit(pageblock_bits)
따라서, pageblock_flags가 가리키는 크기는 64 * 4 = 256bits = 32bytes가 된다.
[7]
usemap
unsigned long*
.
.
.
unsigned long*
unsigned long*
unsigned long*
unsigned long*
.
.
.
usemap
usemap
usemap
unsigned long*
.
.
.
[0]
[15]
[2]
[9]
struct mem_section-> unsigned long *pageblock_flags
이 공간은 아래 코드에 의해 해제됨
free_bootmem(__pa(usemap_map), size);
unsigned long section_mem_map
unsigned long *pageblock_flags
64k = 256MB(section 하나의 크기) / 4k(한 개의 page 크기) = section당 page의 개수
64k / 1k(usemap이 관리하는 page 크기) * 4(한 pageblock당 필요한 flag) = 256 bit
따라서 usemap은 32bytes의 크기를 가짐
enum pageblock_bits { //한 pageblock당 필요한 flag
PB_migrate, = 0
PB_migrate_end = PB_migrate + 3 - 1, = 2
#ifdef CONFIG_COMPACTION
PB_migrate_skip, = 3
#endif /* CONFIG_COMPACTION 선언되어있음. */
NR_PAGEBLOCK_BITS = 4
};
pageblock_bits
enum {
MIGRATE_UNMOVABLE, = 0
MIGRATE_RECLAIMABLE, = 1
MIGRATE_MOVABLE, = 2
MIGRATE_PCPTYPES, = 3 /* the number of types on the pcp lists */
MIGRATE_RESERVE = MIGRATE_PCPTYPES, = 4
MIGRATE_TYPES = 5
};

## Slide 11: 2013.11.30 "arch/arm/mm/init.c"
static void __init arm_bootmem_free(unsigned long min, unsigned long max_low, unsigned long max_high)
NORMAL SIZE = 0x2 F800
max_low – min
0x4 F800 – 0x2 0000
ZONE_SIZE
HIGHMEM SIZE = 0x5 0800
max_high – max_low
0xA 0000 – 0x4 F800
MOVEABE SIZE = 0
enum zone_type { ZONE_NORMAL = 0, ZONE_HIGHMEM = 1, ZONE_MOVABLE = 2, MAX_NR_ZONES = 3 }
phys_addr_t current_limit
struct memblock_type memory
struct memblock memblock;
struct memblock_type reserved
struct memblock_type
unsigned long cnt
unsigned long max
phys_addr_t total_size
struct memblock_region *regions
struct memblock_region
phys_addr_t base
0x2000 0000
phys_addr_t size
0x8000 0000
unsigned long cnt
unsigned long max
phys_addr_t total_size
struct memblock_region *regions
phys_addr_t base
phys_addr_t size
NORMAL SIZE = 0x2 F800
max_low – min
- (low_end - start)
ZHOLE_SIZE
HIGHMEM SIZE = 0
max_high – max_low
– (end - high_start)
MOVEABE SIZE = 0

## Slide 12: 2013.11.30 "mm/page_alloc.c"
static void __meminit calculate_node_totalpages
typedef struct pglist_data {
struct zone node_zones[MAX_NR_ZONES];
struct zonelist node_zonelists[MAX_ZONELISTS];
int nr_zones;
unsigned long node_start_pfn;
unsigned long node_present_pages; /* total number of physical pages */
unsigned long node_spanned_pages; /* total size of physical page range, including holes */
int node_id;
nodemask_t reclaim_nodes; /* Nodes allowed to reclaim from */
wait_queue_head_t kswapd_wait;
wait_queue_head_t pfmemalloc_wait;
struct task_struct *kswapd; /* Protected by lock_memory_hotplug() */
int kswapd_max_order;
enum zone_type classzone_idx;
} pg_data_t;
calculate_node_totalpages 함수에서 초기화
free_area_init_core 함수에서 초기화
free_area_init_core 함수에서 초기화

## Slide 13: 2013.11.30 "mm/page_alloc.c"
static void __paginginit free_area_init_core
struct zone {
/* Fields commonly accessed by the page allocator */
/* zone watermarks, access with *_wmark_pages(zone) macros */
unsigned long watermark[NR_WMARK]; // zone에서 유지해야 할 최소한의 free page 개수를 나타냄.
/*
* When free pages are below this point, additional steps are taken
* when reading the number of free pages to avoid per-cpu counter
* drift allowing watermarks to be breached
*/
unsigned long percpu_drift_mark;
/*
* We don't know if the memory that we're going to allocate will be freeable
* or/and it will be released eventually, so to avoid totally wasting several
* GB of ram we must reserve some of the lower zone memory (otherwise we risk
* to run OOM on the lower zones despite there's tons of freeable ram
* on the higher zones). This array is recalculated at runtime if the
* sysctl_lowmem_reserve_ratio sysctl changes.
*/
unsigned long v[MAX_NR_ZONES];
/*
* This is a per-zone reserve of pages that should not be
* considered dirtyable memory.
*/
unsigned long dirty_balance_reserve;
struct per_cpu_pageset __percpu *pageset;
/*
* free areas of different sizes
*/
spinlock_t lock;
int all_unreclaimable; /* All pages pinned */
/* Set to true when the PG_migrate_skip bits should be cleared */
bool compact_blockskip_flush;
/* pfns where compaction scanners should start */
unsigned long compact_cached_free_pfn;
unsigned long compact_cached_migrate_pfn;
struct free_area free_area[MAX_ORDER];
/*
* On compaction failure, 1<<compact_defer_shift compactions
* are skipped before trying again. The number attempted since
* last failure is tracked with compact_considered.
*/
unsigned int compact_considered;
unsigned int compact_defer_shift;
int compact_order_failed;
struct zone_padding {
char x[0];
} ____cacheline_internodealigned_in_smp;
/* Fields commonly accessed by the page reclaim scanner */
spinlock_t lru_lock;
struct lruvec lruvec;
unsigned long pages_scanned; /* since last reclaim */
unsigned long flags; /* zone flags, see below */
/* Zone statistics */
atomic_long_t vm_stat[NR_VM_ZONE_STAT_ITEMS];
/*
* The target ratio of ACTIVE_ANON to INACTIVE_ANON pages on
* this zone's LRU. Maintained by the pageout code.
*/
unsigned int inactive_ratio;
struct zone_padding {
char x[0];
} ____cacheline_internodealigned_in_smp;
/* Rarely used or read-mostly fields */
/*
* wait_table -- the array holding the hash table
* wait_table_hash_nr_entries -- the size of the hash table array
* wait_table_bits -- wait_table_size == (1 << wait_table_bits)
*
* The purpose of all these is to keep track of the people
* waiting for a page to become available and make them
* runnable again when possible. The trouble is that this
* consumes a lot of space, especially when so few things
* wait on pages at a given time. So instead of using
* per-page waitqueues, we use a waitqueue hash table.
*
* The bucket discipline is to sleep on the same queue when
* colliding and wake all in that wait queue when removing.
* When something wakes, it must check to be sure its page is
* truly available, a la thundering herd. The cost of a
* collision is great, but given the expected load of the
* table, they should be so rare as to be outweighed by the
* benefits from the saved space.
*
* __wait_on_page_locked() and unlock_page() in mm/filemap.c, are the
* primary users of these fields, and in mm/page_alloc.c
* free_area_init_core() performs the initialization of them.
*/
wait_queue_head_t * wait_table;
unsigned long wait_table_hash_nr_entries;
unsigned long wait_table_bits;
/*
* Discontig memory support fields.
*/
struct pglist_data *zone_pgdat;
/* zone_start_pfn == zone_start_paddr >> PAGE_SHIFT */
unsigned long zone_start_pfn;
/*
* spanned_pages is the total pages spanned by the zone, including
* holes, which is calculated as:
* spanned_pages = zone_end_pfn - zone_start_pfn;
*
* present_pages is physical pages existing within the zone, which
* is calculated as:
* present_pages = spanned_pages - absent_pages(pages in holes);
*
* managed_pages is present pages managed by the buddy system, which
* is calculated as (reserved_pages includes pages allocated by the
* bootmem allocator):
* managed_pages = present_pages - reserved_pages;
*
* So present_pages may be used by memory hotplug or memory power
* management logic to figure out unmanaged pages by checking
* (present_pages - managed_pages). And managed_pages should be used
* by page allocator and vm scanner to calculate all kinds of watermarks
* and thresholds.
*
* Locking rules:
*
* zone_start_pfn and spanned_pages are protected by span_seqlock.
* It is a seqlock because it has to be read outside of zone->lock,
* and it is done in the main allocator path. But, it is written
* quite infrequently.
*
* The span_seq lock is declared along with zone->lock because it is
* frequently read in proximity to zone->lock. It's good to
* give them a chance of being in the same cacheline.
*
* Write access to present_pages at runtime should be protected by
* lock_memory_hotplug()/unlock_memory_hotplug(). Any reader who can't
* tolerant drift of present_pages should hold memory hotplug lock to
* get a stable value.
*
* Read access to managed_pages should be safe because it's unsigned
* long. Write access to zone->managed_pages and totalram_pages are
* protected by managed_page_count_lock at runtime. Idealy only
* adjust_managed_page_count() should be used instead of directly
* touching zone->managed_pages and totalram_pages.
*/
unsigned long spanned_pages;
unsigned long present_pages;
unsigned long managed_pages;
/*
* rarely used fields:
*/
const char *name;
} ____cacheline_internodealigned_in_smp;
calculate_node_totalpages 함수에서 초기화
free_area_init_core 함수에서 초기화
free_area_init_core 함수에서 초기화

## Slide 14: 2013.11.30 "mm/page_alloc.c"
static unsigned long __paginginit calc_memmap_size
struct page {
/* First double word block */
unsigned long flags; /* Atomic flags, some possibly
* updated asynchronously */
struct address_space *mapping; /* If low bit clear, points to
* inode address_space, or NULL.
* If page mapped as anonymous
* memory, low bit is set, and
* it points to anon_vma object:
* see PAGE_MAPPING_ANON below.
*/
/* Second double word */
struct {
union {
pgoff_t index; /* Our offset within mapping. */
void *freelist; /* slub/slob first free object */
bool pfmemalloc; /* If set by the page allocator,
* ALLOC_NO_WATERMARKS was set
* and the low watermark was not
* met implying that the system
* is under some pressure. The
* caller should try ensure
* this page is only used to
* free other pages.
*/
};
union {
unsigned counters;
struct {
union {
/*
* Count of ptes mapped in
* mms, to show when page is
* mapped & limit reverse map
* searches.
*
* Used also for tail pages
* refcounting instead of
* _count. Tail pages cannot
* be mapped and keeping the
* tail page _count zero at
* all times guarantees
* get_page_unless_zero() will
* never succeed on tail
* pages.
*/
atomic_t _mapcount;
struct { /* SLUB */
unsigned inuse:16;
unsigned objects:15;
unsigned frozen:1;
};
int units; /* SLOB */
};
atomic_t _count; /* Usage count, see below. */
};
};
};
/* Third double word block */
union {
struct list_head lru; /* Pageout list, eg. active_list
* protected by zone->lru_lock ! */
struct { /* slub per cpu partial pages */
struct page *next; /* Next partial slab */
short int pages;
short int pobjects;
};
struct list_head list; /* slobs list of pages */
struct slab *slab_page; /* slab fields */
};
/* Remainder is not double word aligned */
union {
unsigned long private; /* Mapping-private opaque data:
* usually used for buffer_heads
* if PagePrivate set; used for
* swp_entry_t if PageSwapCache;
* indicates order in the buddy
* system if PG_buddy is set.
*/
struct kmem_cache *slab_cache; /* SL[AU]B: Pointer to slab */
struct page *first_page; /* Compound tail pages */
};
}

## Slide 15: 2013.12.21 "arch/arm/kernel/setup.c“, "kernel/resource.c"
static struct resource * __request_resource(struct resource *root, struct resource *new)
int request_resource(struct resource *root, struct resource *new)
iomem_resource
name “PCI mem”
start 0
end -1
flags IORESOURCE_MEM
parent
child
sibling
name "System RAM"
start memblock.memory.start
end memblock.memory.end
flags IORESOURCE_MEM | BUSY
parent
child
sibling
name "System RAM"
start memblock.memory.start
end memblock.memory.end
flags IORESOURCE_MEM | BUSY
parent
child
sibling
res
res
name "Kernel code"
start virt_to_phys(_text)
end virt_to_phys(_etest-1)
flags IORESOURCE_MEM
parent
child
sibling
code
name "Kernel data"
start virt_to_phys(_sdata)
end virt_to_phys(_end-1)
flags IORESOURCE_MEM
parent
child
sibling
data

## Slide 16: 2013.12.21 "drivers/of/fdt.c"
static unsigned long unflatten_dt_node(struct boot_param_header *blob,
unsigned long mem,
unsigned long *p,
struct device_node *dad,
struct device_node ***allnextpp,
unsigned long fpsize)
*** allnextpp
struct property {
char *name;
int length;
void *value;
struct property *next;
unsigned long _flags;
unsigned int unique_id;
};
struct device_node {
const char *name;
const char *type;
phandle phandle;
const char *full_name;
struct property *properties;
struct property *deadprops; /* removed properties */
struct device_node *parent;
struct device_node *child;
struct device_node *sibling;
struct device_node *next; /* next device of same type */
struct device_node *allnext; /* next in list of all nodes */
struct proc_dir_entry *pde; /* this node's proc directory */
struct kref kref;
unsigned long _flags;
void *data;
};
** allnextp
= ** mynodes
&of_allnodes
&np->allnext
struct device_node *of_allnodes;
np
mem
device _node
full _name
device _node
full _name
np
property
property
property
property

## Slide 17: 2013.12.21 "drivers/of/fdt.c"
static unsigned long unflatten_dt_node(struct boot_param_header *blob,
unsigned long mem,
unsigned long *p,
struct device_node *dad,
struct device_node ***allnextpp,
unsigned long fpsize)
struct property {
char *name;
int length;
void *value;
struct property *next;
unsigned long _flags;
unsigned int unique_id;
};
struct device_node {
const char *name;
const char *type;
phandle phandle;
const char *full_name;
struct property *properties;
struct property *deadprops; /* removed properties */
struct device_node *parent;
struct device_node *child;
struct device_node *sibling;
struct device_node *next; /* next device of same type */
struct device_node *allnext; /* next in list of all nodes */
struct proc_dir_entry *pde; /* this node's proc directory */
struct kref kref;
unsigned long _flags;
void *data;
};
full_name
name
type
phandle
full_name
properties
deadprops
parent
child
sibling
allnext
pde
kref
_flags
data
name
length
value
next
_flags
unique_id
name
length
value
next
_flags
unique_id
name
type
phandle
full_name
properties
deadprops
parent
child
sibling
allnext
pde
kref
_flags
data
property value

## Slide 18: 2014.01.11 "arch/arm/kernel/setup.c"
shift_aff[2]
+
static void __init smp_build_mpidr_hash(void)
struct mpidr_hash {
u32 mask; /* used by sleep.S */
u32 shift_aff[3]; /* used by sleep.S */
u32 bits; /* bits[0] + bits[1] + bits[2] */
};
mask = 각 CPU MPDIR OR 연산한 값
ls
fs[0] =
shift_aff[0]
ls
fs[1]
ls =
fs[2]
bits[0]
bits[1]
shift_aff[1]
ls 와 fs[i] 는 MPIDR 값에 따라 가변적
ls = fls
fs[i] = ffs - 1

## Slide 19: 2014.01.11 "lib/hweight.c"
unsigned int __sw_hweight32(unsigned int w)
unsigned int res = w - ((w >> 1) & 0x55555555);
res = (res & 0x33333333) + ((res >> 2) & 0x33333333);
res = (res + (res >> 4)) & 0x0F0F0F0F;
res = res + (res >> 8);
return (res + (res >> 16)) & 0x000000FF;
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | w = 0xF0F0F0F0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | res = w - ((w >> 1) & 0x55555555);
2 |  | 2 |  | 0 |  | 0 |  | 2 |  | 2 |  | 0 |  | 0 |  | 2 |  | 2 |  | 0 |  | 0 |  | 2 |  | 2 |  | 0 |  | 0 |  | 
+ |  |  |  | + |  |  |  | + |  |  |  | + |  |  |  | + |  |  |  | + |  |  |  | + |  |  |  | + |  |  |  | 
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 
4 |  |  |  | 0 |  |  |  | 4 |  |  |  | 0 |  |  |  | 4 |  |  |  | 0 |  |  |  | 4 |  |  |  | 0 |  |  |  | 
+ |  |  |  |  |  |  |  | + |  |  |  |  |  |  |  | + |  |  |  |  |  |  |  | + |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | res
4 |  |  |  |  |  |  |  | 4 |  |  |  |  |  |  |  | 4 |  |  |  |  |  |  |  | 4 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | res>>8
0 |  |  |  |  |  |  |  | 4 |  |  |  |  |  |  |  | 4 |  |  |  |  |  |  |  | 4 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | res = res + (res>>8)
4 |  |  |  |  |  |  |  | 8 |  |  |  |  |  |  |  | 8 |  |  |  |  |  |  |  | 8 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | res>>16
0 |  |  |  |  |  |  |  | 0 |  |  |  |  |  |  |  | 4 |  |  |  |  |  |  |  | 8 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 
4 |  |  |  |  |  |  |  | 8 |  |  |  |  |  |  |  | c |  |  |  |  |  |  |  | 10 |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 10 |  |  |  |  |  |  |  | = 16
+
+
http://en.wikipedia.org/wiki/Hamming_weight

## Slide 20: 2014.01.11 "mm/percpu.c"
void __init setup_per_cpu_areas(void)
int __init pcpu_embed_first_chunk(size_t reserved_size, size_t dyn_size, size_t atom_size,
pcpu_fc_cpu_distance_fn_t cpu_distance_fn, pcpu_fc_alloc_fn_t alloc_fn, pcpu_fc_free_fn_t free_fn)
static struct pcpu_alloc_info * __init pcpu_build_alloc_info(size_t reserved_size, size_t dyn_size, size_t atom_size,
pcpu_fc_cpu_distance_fn_t cpu_distance_fn)
struct pcpu_alloc_info {
size_t static_size;
size_t reserved_size;
size_t dyn_size;
size_t unit_size;
size_t atom_size;
size_t alloc_size;
size_t __ai_size; /* internal, don't use */
int nr_groups; /* 0 if grouping unnecessary */
struct pcpu_group_info groups[];
};
struct pcpu_group_info {
int nr_units; /* aligned # of units */
unsigned long base_offset; /* base address offset */
unsigned int *cpu_map; /* unit->cpu map, empty
* entries contain NR_CPUS */
};

## Slide 21: 2014.01.11 "mm/percpu.c"
static struct pcpu_alloc_info * __init pcpu_build_alloc_info(
size_t reserved_size, size_t dyn_size,
size_t atom_size,
pcpu_fc_cpu_distance_fn_t cpu_distance_fn)
for_each_possible_cpu(cpu) {
…
for_each_possible_cpu(tcpu) {
…
}
}
tcpu와 cpu의 cpu_distance_fn 함수에 의한 차이가 LOCAL_DISTANCE 이상 벌어지는 경우
group을 하나씩 추가하여 각 그룹으로 나누어줌
0
1
2
3
4
5
6
7
8
9
10
11
12
13
group 0
group 1
ex) LOCAL_DISTANCE 이 6인 경우
[0]
[1]
[2]
[3]
[4]
[5]
[6]
[7]
[8]
[9]
[10]
[11]
[12]
[13]
group_map
group_cnt
0
0
0
0
0
0
0
1
1
1
1
1
1
1
[0]
[1]
[2]
[3]
[4]
[5]
[6]
[7]
[8]
[9]
[10]
[11]
[12]
[13]
7
7
0
0
0
0
0
0
0
0
0
0
0
0
cpu number 0~13

## Slide 22: 2014.01.11 "mm/percpu.c"
static struct pcpu_alloc_info * __init pcpu_build_alloc_info(
size_t reserved_size, size_t dyn_size,
size_t atom_size,
pcpu_fc_cpu_distance_fn_t cpu_distance_fn)
struct pcpu_alloc_info {
size_t static_size;
size_t reserved_size; (8kb)
size_t dyn_size; (12kb)
size_t unit_size; (32kb)
size_t atom_size; (4kb)
size_t alloc_size;
size_t __ai_size; /* internal, don't use */
int nr_groups; /* 0 if grouping unnecessary */
struct pcpu_group_info groups[];
};
struct pcpu_group_info {
int nr_units; /* aligned # of units */
unsigned long base_offset; /* base address offset */
unsigned int *cpu_map; /* unit->cpu map, empty
* entries contain NR_CPUS */
};
pcpu_alloc_info
pcpu_group_info
pcpu_group_info
cpu_map
cpu_map
cpu_map
cpu_map
0
1
…
n
…
cpu numbers…
areas
areas[0]
void **areas
void *areas[groups], base_addr = areas[0], 각각의 CPU 마다 하나의 areas를 가짐.
areas[1]
...
Size = gi->nr_units * ai->unit_size

## Slide 23: 2014.01.25 "mm/percpu.c"
int __init pcpu_setup_first_chunk(const struct pcpu_alloc_info *ai, void *base_addr)
struct pcpu_chunk {
struct list_head list; /* linked to pcpu_slot lists */
int free_size; /* free bytes in the chunk */
int contig_hint; /* max contiguous size hint */
void *base_addr; /* base address of this chunk */
int map_used; /* # of map entries used */
int map_alloc; /* # of map entries allocated */
int *map; /* allocation map */
void *data; /* chunk data */
bool immutable; /* no [de]population allowed */
unsigned long populated[]; /* populated bitmap */
};
pcpu_chunk_struct_size = sizeof(struct pcpu_chunk) + BITS_TO_LONGS(pcpu_unit_pages) * sizeof(unsigned long);
static int smap[PERCPU_DYNAMIC_EARLY_SLOTS] __initdata;
static int dmap[PERCPU_DYNAMIC_EARLY_SLOTS] __initdata;
pcpu_chunk schunk;
pcpu_chunk dchunk;
pcpu_chunk struct
populated[1] …
populated[0]
Slot [13]
Slot [12]
Slot [10]
Slot [9]
Slot [8]
Slot [7]
Slot [6]
Slot [5]
Slot [4]
Slot [3]
Slot [2]
Slot [1]
Slot [0]
32kb
16kb
8kb
4kb
2kb
1kb
512byte
256byte
128byte
64byte
32byte
16byte
8byte
4byte
Chunk slot number
Slot [11]

## Slide 24: 2014.01.25 "mm/percpu.c"
int __init pcpu_setup_first_chunk(const struct pcpu_alloc_info *ai, void *base_addr)
pcpu_chunk schunk;
pcpu_chunk dchunk;
pcpu_first_chunk = dchunk
populated[1] …
populated[0]
Slot [13]
Slot [12]
Slot [10]
Slot [9]
Slot [8]
Slot [7]
Slot [6]
Slot [5]
Slot [4]
Slot [3]
Slot [2]
Slot [1]
Slot [0]
32kb
16kb
8kb
4kb
2kb
1kb
512byte
256byte
128byte
64byte
32byte
16byte
8byte
4byte
Chunk slot number
Slot [11]
areas[0]
areas[0]
...
unit
static
reserved
dynamic
unit
static
reserved
dynamic
...
list
base_addr
각 ai, gi 변수들은 pcpu_* 전역변수에 다 할당하므로,
추후 ai, gi를 위해 할당한 메모리는 free 된다.
pcpu_nr_groups = ai->nr_groups;
pcpu_group_offsets = group_offsets;
pcpu_group_sizes = group_sizes;
pcpu_unit_map = unit_map;
pcpu_unit_offsets = unit_off;
/* determine basic parameters */
pcpu_unit_pages = ai->unit_size >> PAGE_SHIFT;
pcpu_unit_size = pcpu_unit_pages << PAGE_SHIFT;
pcpu_atom_size = ai->atom_size;
pcpu_chunk_struct_size = sizeof(struct pcpu_chunk) +
BITS_TO_LONGS(pcpu_unit_pages) * sizeof(unsigned long);
/*
* Allocate chunk slots. The additional last slot is for
* empty chunks.
*/
pcpu_nr_slots = __pcpu_size_to_slot(pcpu_unit_size) + 2;
pcpu_slot = alloc_bootmem(pcpu_nr_slots * sizeof(pcpu_slot[0]));
/* link the first chunk in */
pcpu_first_chunk = dchunk ?: schunk;
pcpu_chunk_relocate(pcpu_first_chunk, -1);
/* we're done */
pcpu_base_addr = base_addr;

## Slide 25: 2014.02.08 "mm/page_alloc.c"
struct pglist_data
zonelist[0]
zoneref[0]
void __ref build_all_zonelists(pg_data_t *pgdat, struct zone *zone)
static int __build_all_zonelists(void *data)
static void build_zonelists(pg_data_t *pgdat)
struct zonelist {
struct zonelist_cache *zlcache_ptr; // NULL or &zlcache
struct zoneref _zonerefs[MAX_ZONES_PER_ZONELIST + 1];
};
struct zonelist_cache {
unsigned short z_to_n[MAX_ZONES_PER_ZONELIST]; /* zone->nid */
DECLARE_BITMAP(fullzones, MAX_ZONES_PER_ZONELIST); /* zone full? */
unsigned long last_full_zap; /* when last zap'd (jiffies) */
};
struct zoneref {
struct zone *zone; /* Pointer to actual zone */
int zone_idx; /* zone_idx(zoneref->zone) */
};
zone[0]
normal
zone
zone_idx = 1
zone[1]
highmem
zoneref[1]
zone
zone_idx = 0
zoneref[2] (NULL)
zone
zone_idx
zone[2]
movable
zonelist[1]
...

## Slide 26: 2014.02.15 "kernel/mutex.c“, “include/asm-generic/mutex-dec.h”
__mutex_fastpath_lock
__mutex_lock_slowpath
mutex unlock?
(count >= 0 && count == 1?)
이후 count = -1 로 설정됨
선점 불허
wait_lock (스핀락)획득
Dec 방식의 mutex | Lock | Unlock
Fast | 1  0 | 0  1
Slow | 0  -1, -2, -3 -1  1 | -1  0 = 1
Done
task state
UNINTERRUPTIBLE 변경
mutex unlock?
이후 count = -1 로 설정됨
wait_lock 릴리즈
선점 허용
Context Switching 발생
(Mutex Unlock에 의해 Wakeup 을 명시적으로 호출되면 깨어남)
선점 불허
wait_lock 획득
wait_list에서 제거
wait_list 가 비어있으면
count를 0으로 설정
wait_list에 추가
owner 설정
wait_lock 릴리즈
선점 허용
Fast Lock
count 1 감소
count < 0 이면
mutex_lock_slowpath 수행
Slow lock
count를 -1로 설정

## Slide 27: 2014.02.22 "kernel/mutex.c“, “include/asm-generic/mutex-dec.h”
__mutex_fastpath_unlock
__mutex_unlock_slowpath
wait_list 가 비어있는가?
wait_lock (스핀락)획득
Dec 방식의 mutex | Lock | Unlock
Fast | 1  0 | 0  1
Slow | 0  -1, -2, -3 -1  1 | -1  0 = 1
wait_lock 획득
wake_up_process 통해
Task 깨움
count = 1로 설정
Fast unlock
count 1 증가
count <= 0 이면
mutex_lock_slowpath 수행
Slow unlock
wait_lock 릴리즈
Fast unlock은 혼자 mutex
lock, unlock하는 경우 발생
yes

## Slide 28: 2014.02.22 "mm/page_alloc.c“, "kernel/cpu.c“, "kernel/notifier.c"
static int notifier_chain_register(struct notifier_block **nl, struct notifier_block *n)
struct raw_notifier_head {
struct notifier_block __rcu *head;
};
struct notifier_block {
notifier_fn_t notifier_call; (page_alloc_cpu_notify)
struct notifier_block __rcu *next;
int priority;
};
notifier_block
*nl
static int notifier_chain_register(struct notifier_block **nl,
struct notifier_block *n)
{
while ((*nl) != NULL) {
if (n->priority > (*nl)->priority)
break;
nl = &((*nl)->next);
}
n->next = *nl;
rcu_assign_pointer(*nl, n); // *nl = *n
return 0;
}
*next
Priority 3
Notifier_call
notifier_block
*next
Priority 2
Notifier_call
notifier_block
*next
Priority 0
Notifier_call
notifier_block n
*next
Priority 1
Notifier_call
notifier_block
*nl
*next
Priority 3
Notifier_call
notifier_block
*next
Priority 2
Notifier_call
notifier_block
*next
Priority 0
Notifier_call
notifier_block n
*next
Priority 1
Notifier_call

## Slide 29: 2014.03.22 "mm/page_alloc.c"
static inline void __free_one_page(struct page *page, struct zone *zone, unsigned int order, int migratetype)
static inline unsigned long __find_buddy_index(unsigned long page_idx, unsigned int order)
Buddy 찾기
B1 ^ (1 << O) = B2
0 ^ (1 << 5) = 32
32 ^ (1 << 5) = 0
64 ^ (1 << 5) = 96
96 ^ (1 << 5) = 64
128 ^ (1 << 5) = 160
160 ^ (1 << 5) = 128
192 ^ (1 << 5) = 224
224 ^ (1 << 5) = 192
Buddy 시작(부모)찾기
B & ~(1 << O) = P
0 & ~(1 << 5) = 0
32 & ~(1 << 5) = 0
64 & ~(1 << 5) = 64
96 & ~(1 << 5) = 64
128 & ~(1 << 5) = 128
160 & ~(1 << 5) = 128
192 & ~(1 << 5) = 192
224 & ~(1 << 5) = 192
96
64
32
0
224
192
160
128
Order = 5
1 << 5 =32
64
0
192
128
Order = 6
1 << 6 =64
Section 4bit
Zone 2bit
Flags 26
Page flags: | [SECTION] | [NODE] | ZONE | [LAST_NID] | ... | FLAGS |
0
26
27
31

## Slide 30: 2014.03.22 "mm/page_alloc.c"
static inline void __free_one_page(struct page *page, struct zone *zone, unsigned int order, int migratetype)
static inline void set_page_order(struct page *page, int order)
set_page_order
page->private == buddy order
page->_mapcount->counter = -128 (PAGE_BUDDY_MAPCOUNT_VALUE)
if ((order < MAX_ORDER-2) && pfn_valid_within(page_to_pfn(buddy))) {
struct page *higher_page, *higher_buddy;
combined_idx = buddy_idx & page_idx;
higher_page = page + (combined_idx - page_idx);
buddy_idx = __find_buddy_index(combined_idx, order + 1);
higher_buddy = higher_page + (buddy_idx - combined_idx);
if (page_is_buddy(higher_page, higher_buddy, order + 1)) {
list_add_tail(&page->lru,
&zone->free_area[order].free_list[migratetype]);
goto out;
}
}
list_add(&page->lru, &zone->free_area[order].free_list[migratetype]);
Higerpage가 버디이면 해당 page는 merge될 가능성이 높으므로 list 뒤에 넣고,
버디가 아니라면 그냥 list에 추가한다.
96
64
32
0
224
192
160
128
Order = 5
1 << 5 =32
Page_idx
&Higher_page
= combined_idx
= Buddy_idx(1)
Buddy_idx(2)
= &Higher_buddy
64
0
192
128
Order = 6
1 << 6 =64
Page_idx
&Higher_page
= combined_idx
= Buddy_idx(1)
Buddy_idx(2)
= &Higher_buddy

## Slide 31: 2014.03.29 “mm/bootmem.c”
static unsigned long __init free_all_bootmem_core(bootmem_data_t *bdata)
map = bdata->node_bootmem_map;
vec = ~map[idx / BITS_PER_LONG];
11111111 11111111 11111111 11111111
Vec가 모두 1이면 2^5 만큼 한꺼번에
page free - buddy로 만듬
if (IS_ALIGNED(start, BITS_PER_LONG) && vec == ~0UL) {
int order = ilog2(BITS_PER_LONG);
/*! 20140322 BITS_PER_LONG: 32, order: 5 */
__free_pages_bootmem(pfn_to_page(start), order);
count += BITS_PER_LONG;
start += BITS_PER_LONG;
}
11100111 11111101 11110111 11111111
Vec가 모두이 아니면 0이 아닌 각 페이지 하나하나를
page free - buddy로 만듬
else {
unsigned long cur = start;
start = ALIGN(start + 1, BITS_PER_LONG);
while (vec && cur != start) {
if (vec & 1) {
page = pfn_to_page(cur);
__free_pages_bootmem(page, 0);
count++;
}
vec >>= 1;
++cur;
}
}

## Slide 32: 2014.03.29 “mm/page_alloc.c”
void free_hot_cold_page(struct page *page, int cold)
static void free_pcppages_bulk(struct zone *zone, int count, struct per_cpu_pages *pcp)
struct per_cpu_pages {
int count; /* number of pages in the list */ 현재 가지고 있는 page 수
int high; /* high watermark, emptying needed */ pcpu가 가질 수 있는 최대 page 수
int batch; /* chunk size for buddy add/remove */ count > high 였을 때 buddy로 넘길 page 수
/* Lists of pages, one per migrate type stored on the pcp-lists */
struct list_head lists[MIGRATE_PCPTYPES];
};
pcp = &this_cpu_ptr(zone->pageset)->pcp;
list = &pcp->lists[migratetype];
- - - count > high 인 경우 free_pcppages_bulk를 통해 아래 루틴 수행
while (to_free) {
비어있지 않은 lists[n] 선택
lists[1], [2] 가 비어있으면 batch_free = to_free 로 치환
do { free page } while (--to_free && --batch_free && !list_empty(list));
}
enum {
MIGRATE_UNMOVABLE, = 0
MIGRATE_RECLAIMABLE, = 1
MIGRATE_MOVABLE, = 2
MIGRATE_PCPTYPES, = 3 /* the number of types on the pcp lists */
MIGRATE_RESERVE = MIGRATE_PCPTYPES, = 4
MIGRATE_TYPES = 5
};
Ex) count (batch = to_free) 가 5 인 경우
lists[0]
lists[1]
lists[2]
1단계
2단계
3단계
4단계
5단계
6단계
lists[0]
lists[1]
lists[2]
1단계
2단계
3단계
4단계
zone->free_area[order].free_list[migratetype]

## Slide 33: 2014.03.29 “arch/arm/mm/init.c”
static void __init free_highpages(void)
for_each_memblock(reserved, res) {
if (res_end < start)
continue; // reserved1 인 경우 무시됨
if (res_start < start)
res_start = start; // reserved2 인 경우
if (res_start > end)
res_start = end; // reserved5 인 경우
If (res_end > end)
res_end = end; // reserved4, reserved5 인 경우
If (res_start != start)
free_area_high(start, res_start); // reserved(앞쪽) 아닌 영역을 Free하겠다는 의미
start = res_end;
if (start == end)
break;
}
If (start < end)
free_area_high(start, end); // reserved(뒤쪽) 아닌 영역을 Free 하겠다는 의미
highmem
memblock
lowmem
reserved3
res_start
res_end
reserved2
reserved4
start
end
reserved1
reserved5
Free되는 영역

## Slide 34: 2013.11.30 "mm/page_alloc.c"
static unsigned long __paginginit calc_memmap_size
struct page {
/* First double word block */
unsigned long flags; /* Atomic flags, some possibly
* updated asynchronously */
struct address_space *mapping; /* If low bit clear, points to
* inode address_space, or NULL.
* If page mapped as anonymous
* memory, low bit is set, and
* it points to anon_vma object:
* see PAGE_MAPPING_ANON below.
*/
/* Second double word */
struct {
union {
pgoff_t index; /* Our offset within mapping. */
void *freelist; /* slub/slob first free object */
bool pfmemalloc; /* If set by the page allocator,
* ALLOC_NO_WATERMARKS was set
* and the low watermark was not
* met implying that the system
* is under some pressure. The
* caller should try ensure
* this page is only used to
* free other pages.
*/
};
union {
unsigned counters;
struct {
union {
/*
* Count of ptes mapped in
* mms, to show when page is
* mapped & limit reverse map
* searches.
*
* Used also for tail pages
* refcounting instead of
* _count. Tail pages cannot
* be mapped and keeping the
* tail page _count zero at
* all times guarantees
* get_page_unless_zero() will
* never succeed on tail
* pages.
*/
atomic_t _mapcount;
struct { /* SLUB */
unsigned inuse:16;
unsigned objects:15;
unsigned frozen:1;
};
int units; /* SLOB */
};
atomic_t _count; /* Usage count, see below. */
};
};
};
/* Third double word block */
union {
struct list_head lru; /* Pageout list, eg. active_list
* protected by zone->lru_lock ! */
struct { /* slub per cpu partial pages */
struct page *next; /* Next partial slab */
short int pages;
short int pobjects;
};
struct list_head list; /* slobs list of pages */
struct slab *slab_page; /* slab fields */
};
/* Remainder is not double word aligned */
union {
unsigned long private; /* Mapping-private opaque data:
* usually used for buffer_heads
* if PagePrivate set; used for
* swp_entry_t if PageSwapCache;
* indicates order in the buddy
* system if PG_buddy is set.
*/
struct kmem_cache *slab_cache; /* SL[AU]B: Pointer to slab */
struct page *first_page; /* Compound tail pages */
};
}

## Slide 35: 2014.04.05 “mm/slub.c”, “include/linux/slub_def.h”
void __init kmem_cache_init(void)
/*
* Slab cache management.
*/
struct kmem_cache {
struct kmem_cache_cpu __percpu *cpu_slab;
/* Used for retriving partial slabs etc */
unsigned long flags;
unsigned long min_partial;
int size; /* The size of an object including meta data */
int object_size; /* The size of an object without meta data */
int offset; /* Free pointer offset. */
int cpu_partial; /* Number of per cpu partial objects to keep around */
struct kmem_cache_order_objects oo; /* the order and the number of objects */
/* Allocation and freeing of slabs */
struct kmem_cache_order_objects max;
struct kmem_cache_order_objects min;
gfp_t allocflags; /* gfp flags to use on each alloc */
int refcount; /* Refcount for slab cache destroy */
void (*ctor)(void *);
int inuse; /* Offset to metadata */
int align; /* Alignment */
int reserved; /* Reserved bytes at the end of slabs */
const char *name; /* Name (only for display!) */
struct list_head list; /* List of slab caches */
#ifdef CONFIG_SYSFS
struct kobject kobj; /* For sysfs */
#endif
struct kmem_cache_node *node[MAX_NUMNODES];
};
struct kmem_cache_cpu {
void **freelist; /* Pointer to next available object */
unsigned long tid; /* Globally unique transaction id */
struct page *page; /* The slab from which we are allocating */
struct page *partial; /* Partially allocated frozen slabs */
};
order (상위 16bit) / the number of objects (하위 16bit = 한 slab에 몇 개의 object가 들어갈 수 있는지..)
struct kmem_cache_order_objects {
unsigned long x;
};
struct kmem_cache_node {
spinlock_t list_lock;
#ifdef CONFIG_SLUB
unsigned long nr_partial;
struct list_head partial;
#ifdef CONFIG_SLUB_DEBUG
atomic_long_t nr_slabs;
atomic_long_t total_objects;
struct list_head full;
#endif
#endif
};

## Slide 36: 2014.04.05 “mm/slub.c”, “include/linux/slub_def.h”
void __init kmem_cache_init(void)
kmem_cache_node = &boot_kmem_cache_node;
struct kmem_cache {
struct kmem_cache_cpu __percpu *cpu_slab;
/* Used for retriving partial slabs etc */
unsigned long flags; = SLAB_HWCACHE_ALIGN
unsigned long min_partial; = 5
int size; /* The size of an object including meta data */ = kmem_cache_node 구조체 크기 (40)
int object_size; /* The size of an object without meta data */ = kmem_cache_node 구조체 크기
int offset; /* Free pointer offset. */
int cpu_partial; /* Number of per cpu partial objects to keep around */ = 30
struct kmem_cache_order_objects oo; = 102
/* Allocation and freeing of slabs */
struct kmem_cache_order_objects max; = 102
struct kmem_cache_order_objects min; =
gfp_t allocflags; /* gfp flags to use on each alloc */
int refcount; /* Refcount for slab cache destroy */
void (*ctor)(void *);
int inuse; /* Offset to metadata */
int align; /* Alignment */
int reserved; /* Reserved bytes at the end of slabs */ = 0
const char *name; /* Name (only for display!) */ = "kmem_cache_node"
struct list_head list; /* List of slab caches */
#ifdef CONFIG_SYSFS
struct kobject kobj; /* For sysfs */
#endif
struct kmem_cache_node *node[MAX_NUMNODES];
};

## Slide 37: 2014.04.12 “page_alloc.c”
static inline struct page *__rmqueue_smallest(struct zone *zone, unsigned int order, int migratetype)
static inline void expand(struct zone *zone, struct page *page, int low, int high, struct free_area *area, int migratetype)
area = &(zone->free_area[current_order]); // ex) current_order = 0
free_area[4]
free_area[4]
free_area[3]
page[size]
free_area[4]
free_area[3]
free_area[2]
page[size]
free_area[4]
free_area[3]
free_area[2]
free_area[1]
Page[size]
free_area[4]
free_area[3]
free_area[2]
free_area[1]
free_area[0]
frea_area[0] 이 empty로 되어있기 때문에
expand 함수가 수행된다.
빨간색 부분이 __rmqueue_smallest 함수의 리턴값이 되고, 나머지 부분이 buddy로 expand 된다.

## Slide 38: 2014.04.26 “mm/slub.c”
static struct page *new_slab(struct kmem_cache *s, gfp_t flags, int node)
last = start;
// for_each_object(p, s, start, page->objects) {
for (p = (start); p < (start) + (page->objects) * (s)->size; p += (s)->size) {
setup_object(s, page, last);
set_freepointer(s, last, p); // *(void **)(last + s->offset) = p;
last = p;
}
setup_object(s, page, last); set_freepointer(s, last, NULL);
page->freelist = start; page->inuse = page->objects; page->frozen = 1;
...
object
object
object
object
P = last
p
...
object
object
object
object
p1
page
size
주황색 공간은 metadata를 위한 공간
metadata가 없으면 s->offset 은 0이 된다.
0인경우의 예이며 0이 아닌 경우 ------------>
p1
...
object
object
object
object
p2
p1
p2
1st for
2nd for
3rd for
...
object
object
object
p
p1
p2
last for
null
last
last
last
pn
kmem_cache
p
s->offset
size = kmem_cache size + metadata

## Slide 39: 2014.04.26 “mm/slub.c”
static void early_kmem_cache_node_alloc(int node)
static inline void add_partial(struct kmem_cache_node *n, struct page *page, int tail)
...
kmem_cache_node
Object
추후에 kmem_cache_node로 사용될..
object
object
partial
Page 1
struct kmem_cache *slab_cache
struct list_head lru
Page 2
struct kmem_cache *slab_cache
struct list_head lru
...
object
object
object
object
Slab in page 1
Slab in page 2

## Slide 40: 2014.05.31 “mm/slub.c”
static inline void flush_slab(struct kmem_cache *s, struct kmem_cache_cpu *c)
static void deactivate_slab(struct kmem_cache *s, struct page *page, void *freelist)
struct kmem_cache *s, kmem_cache_cpu *c;
deactivate_slab(s, c->page, c->freelist);
Stage 1
object
object
object
object
object
object
object
freelist
prior = page->freelist = NULL
object
NULL
object
object
object
object
object
object
freelist
prior = page->freelist
nextfree
nextfree
object
NULL
object
object
object
object
object
object
freelist
prior = page->freelist
nextfree
object
NULL
object
object
object
object
object
object
prior = page->freelist
freelist = nextfree
………for 문…………

## Slide 41: 2014.05.31 “mm/slub.c”
static inline void flush_slab(struct kmem_cache *s, struct kmem_cache_cpu *c)
static void deactivate_slab(struct kmem_cache *s, struct page *page, void *freelist)
struct kmem_cache *s, kmem_cache_cpu *c;
deactivate_slab(s, c->page, c->freelist);
Stage 2
object
NULL
object
object
object
object
object
object
old.prelist = page->freelist
freelist